Oklahoma Tax Commission Online Payment System

Receipt Printer Setup

(Epson TM-U220D Receipt Printer)

This document outlines setting up the Epson TM-U220D for use with the OK.gov Tax payment web application.  This involves downloading drivers form the OK Tax payment site, install the Epson printer drivers and configuring the web browser to print on the receipt printer correctly.

Downloading the printer drivers

- Open your web browser and enter this URL in the address bar: http://www.ok.gov/oktax/payment/Epson.zip  This will prompt you to download the zip file.  You will need to save it to your desktop..

- After  you have downloaded the zip file you will need to unzip or extract the zip into a folder on your Desktop.  Name the folder ‘EpsonDrivers’.

- Now open the folder and you will see several pdf documents and three installation programs…

- Once you see all the files you will need to run the setup program ‘ATM_304E.exe’…

Select that you accept the license agreement and click next

- Step through the installation with the following screens….

Chose the installation folder.  The folder that the setup program presents is fine for this installation.

The installation process will start extracting files

Once the installation is finished it will prompt you for a series of questions…

Select the operating system that you are installing the printer on.

This window will allow you to select the driver and settings for the printer.  In this list you will need to place a check mark next to ‘(Ver. 2.XX compatible APD) Epson TM-U220 Receipt’.  Once you have placed a check mark next to this driver you will need to click on the button below labeled ‘Printer Port Settings, e.t.c….’.

The screen that pops up will allow you to configure the serial port and all of the associated settings to connect to the printer.

On this screen you will need to select the following settings..

Serial: 		‘COM1’

BaudRate: 		‘9600’

DataBits; 		‘8’

Parity: 		‘None’

StopBits: 		‘1’

FlowControl: 	‘DTR/DSR’

The following screens show the flow of the installation program…

Once you have changes these settings you will need to click the ‘OK’ button.  This will return you to the previous screen.  At this point you can click on ‘Finish’…

After clicking finish, the installation program will continue to setup the printer…

Once the installation is completed you will be asked to restart your computer.  If you do not restart your computer your new installed printer will not work.  If you can not restart your computer after the installation is completed, you can simply elect not to restart and restart later when you are able to….

After the computer restarts, we need to test the printer to see if we can print to it.  Once your at your desktop, click on ‘Start-Settings-Printer and Faxes’….

You should see the newly installed printer…

At this point you will need to right click on the printer and click on ‘Properties’…

Click on ‘Print Test Page’…

Once the printer prints a windows test page you can click on ‘OK’…

Setting up Internet Explore and Firefox for Receipt Printer

- Once your printer is setup on your PC, you will need to obtain a login for the OK Tax web application.

- When you are logged into the application it will take you to the main menu.

- To setup the web browser you will need to click on ‘File-Page Setup’.

- this screen will allow you to change the Margins and the header and footer information.  Change the follow information fields to:

the header and footer field needs to be blank

All margins need to be set to ‘0.25’…

This screen shot shows the Firefox page setup…

- Now Click ‘OK’.

- Now you will need to set the OK Tax web application to format the receipts to print to the new receipt printer.  From the main menu you will need to click on ‘Select Printer’….

- By default the ‘PC Printer’ is selected.  You will need to select the ‘Terminal Printer (Paper Rolls)’ and click ‘Save’.

At this point your new receipt printer is setup and ready to use.